## Slide 1: Gamma Spectroscopy
4/26/12
H. Herrmann (LANL)

## Slide 2
e-
Next Steps
Cherenkov detectors
Energy thresholded
Gas limited to >2.5 MeV
Solid limited to <~0.2 MeV
Aerogel might span the gap
Real g-ray spectroscopy (Energy resolved)
X-ray framing camera + CCD
Source
θBragg=12o
Sagittally Bent HOPG crystal
M. Moran, RSI 56, 1066 (1985)
Compton Spect. (>2 MeV)
Pixelated Single-Hit “Furlong” (>0.1 MeV?)
Bent Crystal
(<1.5 MeV)

## Slide 3: Energy resolution would provide valuable information to the Ignition Campaign
DT Fusion
D(n,)
12C(n,)
12C(n,n’)
12C(n,)
Hohlraum/TMP n-
Calculated DT Gamma-Ray Spectrum
Spectral uncertainties call for energy resolution
  GRH is only energy thresholding, not resolving
  Be Ablator R from impurity 16O(n,n’) at 6.1, 6.9, 7.1 MeV
  Spectral lines may provide:
    16.75 MeV fusion   DT yield
    4.44 MeV 12C(n,n’)  CH Ablator R
    15.58 MeV D(n,)  Fuel R
Notes: 3

## Slide 4
DT Fusion -ray spectrum needs to be mapped out better
D + T  5He*
5He*
16.75 MeV
4.5 MeV
0 MeV
-0.96 MeV
4He + n
5He
1
0
1/0  2.3 ± 0.4
1
0
G-total/Gn = (4.2 ± 2.0) × 10-5
Y. Kim (LANL), C. Horsfield (AWE)
GCD mapping of  spectrum at OMEGA used assumed line shapes determined by R-Matrix analysis (G. Hale, LANL
Needs to be verified by spectroscopy

## Slide 5
0.5 MeV resolution (E/E  3%) at high energy is adequate

## Slide 6
0.5 MeV resolution (E/E  3%) at high energy is adequate

## Slide 7
0.5 MeV resolution at low energy (adequate, but GCS will do better at 3%)

## Slide 8: Mix-dependant -ray lines could aid Ignition Campaign
reaction | Eg (MeV) | Application
13C(d,n)14N* | 4.91, 5.69 | 13C layers in CH or doped in Be
9Be(d,n)10B* | 2.8, 3.4 , 4.49, 6.03 | Be Capsule
9Be(a,n)12C* | 4.4 | Be Capsule
MeV alpha-particles born in the DT burn and MeV knockon deuterons and tritons interacting with ablator material (C or Be)
Reactions emitting gammas sensitive to stopping power with sg>~10 mb/sr/gamma-ray:
A. Hayes, LANL

## Slide 9: Challenge: measure high energy -ray in background of other -rays & LPI x-rays
2-Temp LPI x-rays spectrum (Kruer model)
  3 orders-of-mag more x-ray energy below 300 keV than above
  Nearly 4 orders-of-mag more energy in LPI x-rays than Prompt Nuclear -rays
  Comparable energy in x-rays & -rays above ~300 keV
    Empirically, there’s ~3x more FFLEX signal from -rays than x-rays at >250 keV
    GRH background is dominated by <250 keV x-rays
-rays of interest:
12C(n,n’)
DT-  D(n,)

## Slide 10
Physics-based Requirements:
Topic | Requirement
Resolution | E/E  5%
Sensitivity Req’d n Yield | 100 e- in bins of interest: Y > 3e14 for 12C- (at R12C 200 mg/cm2) Y > 3e15 for DT-0 Y > 1e16 for DT-1 and D(n,g)
Binning | 12 energy bins
Temporal Response | <1ns
SNR | >5
Energy Range | Total: 2-25 MeV Single Shot: 2/3Ehigh to Ehigh (e.g., 12-18 MeV)

## Slide 11
Option: FURLONG, does not need high neutron yield…
Each detector records less than one gamma ray, many detectors.
Build a spectrum by summing over many detectors.
Painful, but very high quality data.
LaBr3 “Brilliance” detectors.
The Best…. But VERY expensive.
Need to build factory, share with GSI / FAIR plans
Very good energy resolution
Detector array planned at FAIR
W. Stoeffl (LLNL)