## Slide 2
Drivers
Advances in High Energy Density Physics Require:
•Targets
Theory
Targets
Diagnostics
Given a driver, innovation in targets and diagnostics drive new science

## Slide 3: Experimental measurements drive ICF: theory is a guide
• Sixties – Magnetic fusion development of high temperature plasma diagnostics
• Seventies- nuclear test and ICF diagnostic development started- borrowed from MFE
• Eighties - Nuclear Test Measurements
• Nineties and First decade- Nova, OMEGA, led to initial NIF diagnostics
• What next ?
Diagnostics you invent for the second decade will challenge theory/simulations and drive HED science

## Slide 4: NIF supports ~50 sophisticated diagnostics for users (through ~ 2012 : more to come)
Kilkenny - NIF Diagnostics Discussion, Jan. 30, 2012
4
NIF-0112-24078.ppt
Optical ~7 : Backscatter, into and close to lenses, VISAR and Streaked Optical Pyrometer, 4w fiducials
X-ray ~25: Gated and streaked imaging and spectroscopy, absolute time resolved x-ray band spectrometers
Nuclear ~15: Neutron yield, spectroscopy and imaging, radio-chemistry, proton temporal and spectral, time resolved gamma band spectroscopy
Diagnostic operations: facility operations and data acquisition
Most were developed at NTS, Nova or OMEGA
Kilkenny - BOG S&T, July 12-13, 2011
4
NIF-0711-22517.ppt
X-ray imagers and
MRS foil on NIF

## Slide 5
Author—NIC Review, December 2009
5
NIF-0000-00000s2.ppt
We have multiple redundant diagnostics of the key attributes of the DT implosions- to cross check values
THS
(reactivity)
rRHS
(bootstrap heating)
rRTotal
(confinement)
DRmix/DRshell
(confinement)
RHS
(convergence)
Hot Spot |  | 
THS | 4.5 keV | NTOF20, hGXI, ARIANE,DIXI
<RHS> | 25µm | hGXI, ARIANE, DIXI, NI
Yn | 1014-19 | NToF, NAD, MRS, CR39
tburn,bang | <100 ps, ~20ns | hGXI, SPBT, NToF4BT, GRH, SPIDER
mix | 30% | hGX, ARIAN,DIXI, HEXRS,GRH
Cold Fuel |  | 
<rR> | > 1.7 g/cm2 | NToF20,3.9, WRF MRS, RAGS, ARC, NI, GRH
DrR(q) | < 0.4 g/cm2 | ARC, NI
DRmix/DRshell | < 0.25 | hGXI
5
NIF-1209-17998.ppt
Kilkenny—NIC Review, December 9–11, 2009
Theoretical view: correct ??

## Slide 6: Complementary redundant diagnostics are essential for the scientific method
Karl Popper, Hutchinson Press, 1959: ”cannot prove a theory (measurement) is right, can prove it is wrong”- by test ( comparison with other diagnostics
NIF-1209-17998.ppt
Kilkenny, NIC Review, December 9–11, 2009
6
• Down Scatter Fraction (DSF): measure
by NToF and Magnetic Recoil Spectrometer
• rR: measure with NToF, MRS, Radchem
and by ARC
• Hot spot T measured by x-rays
and neutron emission
Falsifiability and Testability
: “Hypotheses are nets: only he who casts will catch”

## Slide 7: NIF diagnostics engage the user community, and is major effort by the community: > 200 scientists and engineers at LLNL, LLE, MIT, LANL,SNL, GA, AWE, CEA
• About 50 diagnostics systems have been implemented over the last 5 years. Proposed by community. Scope driven by ICF and SSP programs, reviewed by community

## Slide 8: Major contributions from MIT

## Slide 9: LLNL’s new Director, Parney Albright (theoretician), receives a copy of Casey’s thesis, NIF’s first Ph. D.
Alex
Zylstra
Dan
Casey
Parney
Albright
I would like to thank all of you for the excellent and comprehensive tour of the NIF diagnostics systems. The combined science and engineering that has gone into these systems has effectively provided the “eyes and ears” of the NIF enterprise and a foundational element of all NIF experiments. As we discussed, I would like to hear more about the opportunities for next-generation diagnostics with the essential overlay of a strong mission/programmatic “pull” for advanced diagnostics investments. I continue to be wowed by the accomplishments of team NIF and this tour was no exception. Regards, Parney

## Slide 10: DSR that Nino went on about: down scattered neutrons are generated by scattering of the primary neutrons off the cold fuel- measure rR
Down-scatter ratio (DSR) technique
DSR = (10-12MeV) / (13-15MeV), r Rfuel = 21 DSR gm /cm2
Some variation of rR with direction is be measured from DSR(q,f)
10

## Slide 11: Major diagnostic contributions from LLE

## Slide 12: LLE: Special capsules and spectrometer have been designed to trace origin of ablator mix in the hot spot
1
2
3
4
5
layer | dopant (atomic %)
1 | Cu(0.1%)
2 | Si(0.7%) Ge(0.15%)
3 | Si(1.7%) Ge(0.15%)
4 | Si(1%)
5 | none
Cu, Ge, Si doped CH ablator
Supersnout II (5.75 – 16.5 keV)
Development of spectrometer by Sean R. will enable
x-ray Thomson scattering on NIF and OMEGA

## Slide 13: South pole bang time x-ray detector robustly measures x-ray and neutron bang-time:- LLE/LLNL
South pole bang time detector looks up the hohlraum axis, sees implosion
Kilkenny - NIF Diagnostics Discussion, Jan. 30, 2012

## Slide 14: Major contributions from LANL and SNL

## Slide 15: Diagnostics evolve and generate new programs and scope. In general, diagnostics are used beyond their original scope.
Examples of evolution of diagnostics
  Gamma Reaction History, discovered uncertainty in the branching ratio, led to the Gamma Compton Spectrometer - Hans Hermann tomorrow
  NToF led to use for DSR, led to neutron backscatter edge and low energy neutron spectroscopy
  GXD led to hGXI led to ARIANE led to DIXI
  HEXRS led to super-snout 1 and 2 and then to high resolution spectroscopy, x-ray Thomson scattering- Sean Regan
We've taken NTS/Omega/Nova concepts, built a new generation of instruments. BUT they are old. We need a new set of diagnostics for our three superb facilities

## Slide 17: Evolutionary improvement of NToF: back scattered and down scattered neutrons probe different cold fuel regions
neutrons
17
neutrons
nT back scatter 3.5 MeV
nD back scatter 1.6 MeV
nT and nD down scatter 10 – 12 MeV
Chart: 
DT neutrons from Hot Spot 14 MeV
D2 neutrons from Hot Spot 2.45 MeV
neutrons
NToF - logarithmic
17

## Slide 19: How we decided the NIF diagnostics so far
NIC EP and the NIF CDR contained the primary, requirements driven NIC implosion diagnostics.
NIC EP had a conceptual agreement for partners to contribute
6 Diagnostics workshop 2008 – 2011 refined requirements, defined diagnostics, scoped resources, reached inter-lab agreements on resource commitments, explored analysis routines and calibrations
  Examples:
      Neutron Imager- LANL
      Magnetic Recoil Spectrometer- MIT & LLE
      NToF- LLE
      NAD – SNL
• Evolutionary diagnostics were agreed and assigned
      Hard Xray spectrometer- LLE
      WRF- MIT – SPIDER-SL
Community assignment of diagnostics success of NIF

## Slide 20: Some of the existing diagnostics are foundational
20
MCP Module
CCD Camera
MCP Pulser Electronics
CCD Power Supply
Embedded Computer
Gated x-ray cameras widely used
Although widely used at the moment they are middle aged

## Slide 21: Some of the existing diagnostics are foundational
Kilkenny - NIF Diagnostics Discussion, Jan. 30, 2012
21
NIF-0112-24078.ppt
21
Although widely used at the moment they are middle aged
VISAR used for ignition, WCI and Basic Science

## Slide 22: What next ? The next set of diagnostics will be chosen to satisfy NIF’s missions in the second decade
Science Use
MTF 10.1: ICF
MTF 10.2:HED
Use theory/simulations to generate requirements- pinch of salt

## Slide 23: Future diagnostics: “build and they will come” or ask designers what they want
• Simulations/theory are challenged in driving innovation. Theory sometimes follows.
• Sometimes, theory gets in the way. E.g. areal density difference in DSR vs. angular position cant be explained by theory and “so the “measurements must be wrong”
• Need balance between mission requirements and diagnostic technology push
“As we discussed, I would like to hear more about the opportunities for next-generation diagnostics with the essential overlay of a strong mission/programmatic “pull” for advanced diagnostics investments.
Regards, Parney” ( A theoretician !)
Our job as experimentalists is to challenge accepted theory with
clever experiments and measurements

## Slide 24: Much of what we know about the universe comes from telescopes
• Telescopes evolved slowly over several centuries
• Our atmosphere restricted studies of the universe to the visible
Space flight changed all that

## Slide 25: Shuttle enabled NASA’s Great Observatories covering the spectrum from g s to the infrared and opened our eyes on the Universe
Kilkenny - NIF Diagnostics Discussion, Jan. 30, 2012
25
NIF-0112-24078.ppt
Just as the great observatories exploited space flight, so the great
observatories- diagnostics on NIF and OMEGA should enable
discovery science in the laboratory

## Slide 26: NASA’s Great Observatories, are four space-borne observatories measuring in four different bands: visible, gamma rays, x-ray, and infrared)
Hubble Space Telescope: 2.4 m optical: star birth,
star death, and galaxy evolution, and has helped
move black holes from scientific theory to fact.
The Compton Gamma Ray Observatory:
violent physical processes in the Universe,
emitting g ‘s
Chandra x-ray observatory : X-ray telescopes.
Detailed studies of black holes, supernovas,
and dark matter.
The Spitzer Space Telescope: infrared

## Slide 27
What could we do ? The 7th NIF diagnostic workshop 5/14–6/16 We have started process for diagnostic plan beyond 2012
New diagnostics proposed | #
Neutron spectroscopy | 7
Neutron/gamma imaging | 2
Radio-chemistry | 2
Gamma spectroscopy | 5
Optical: interferometry, Faraday,Thomson | 3
X-ray spectroscopy | 9
X-ray imaging | 8
Manipulators | 2
Kilkenny - NIF Diagnostics Discussion, Jan. 30, 2012
27
NIF-0711-24080.ppt

## Slide 28
gain
X-ray microscopes_ what do we do ? NIF and OMEGA’s
x-ray movies were really good in the early nineties

## Slide 29: NIF: x-ray movies from 120321: ITFX =0.1 but kidney shaped
Polar View
Equatorial View
We are developing the Chandra observatory of ICF

## Slide 30: NIF’s Chandra?
• KB optic coated for 10 -15 keV, dx ~ 3 micron
• Fielding on DIM at 10 -20 cm
• Image at ~ 7 m
• n and gamma screened detector
• True framing camera detector dt ~ 100 ps

## Slide 31: What is the ICF analogy of Hubble? new optical diagnostics will be foundational for NIF
Thomson scattering used for all missions
Optical probe for interferometry, Faraday
Should we use a soft
X-ray laser?

## Slide 32: An energy-resolving Gamma Compton Spectrometer (GCS) : LANL, LLNL, GA & NSTec
DT Fusion
D(n,)
12C(n,)
12C(n,n’)
12C(n,)
Hohlraum/TMP n-
Calculated DT Gamma-Ray Spectrum
Spectral uncertainties call for energy resolution
  GRH is only energy thresholding, not resolving
  Spectral lines may provide:
    DT yield from 16.75 MeV fusion line
    Fuel rhoR from D(n,) 15.58 MeV line
    Ablator rhoR from 12C(n,n’) 4.44 MeV line
    Additional nuclear physics outside of NIC campaign
Gamma Compton Spectrometer
Requirements
  Yield >1e16 DTn
  Energy Resolution  0.5 MeV
  <1ns temporal response
  Tunable energy range (1-20 MeV)

## Slide 33: Gamma ray spectroscopy, single hit pixelated detector, conceptualized as a multi-purpose new 260 m detector station
New detector station will be multi-purpose and will
require a broad user community support
260 meter
DT Fusion
D(n,)
12C(n,)
12C(n,n’)
12C(n,)
Hohlraum/TMP n-
Calculated DT Gamma-Ray Spectrum

## Slide 34: A new set of “great observatories” diagnostics will explore the physics of the Universe using NIF, OMEGA & Z
X-rays – NIF has > 10 mm pinhole cameras, single frame dt ~ 100 psec
and low resolution spectroscopy
- `NIF needs dx ~ 2 mm, dt ~10 psec with real framing, l/dl ~10,000
Gammas - NIF, OMEGA has several MeV resolution, dt ~ 10s psec
- NIF, OMEGA needs 0.1 MeV resolution, dt ~ 10 psec.
Optical - NIF, OMEGA has a limited interferometry (f/3.3, 600 nm VISAR)
-NIF, OMEGA needs Thomson, interferometry/Faraday into u.v.
Neutrons- NIF has medium energy spectrometers, 20 mm static imaging
- NIF needs good sub-MeV resolution, versatile imaging
,
Foundational diagnostics need technology basis, consensus, phasing(W, Z) and long term commitment