## Slide 1: Beyond Bateman: 10x higher Q.E. MCPs at 10 - 100 keV
Unity gain thick MCP (DC)
Electron multiplier MCP (Gated)
hn
Phosphor
Future: Two MCP (Proximity focus coupling)?
N. Izumi, 2011
Time-discriminating detectors will be needed even at high photon energy when sources to be backlit or other sources have strong self-emission (hohlraums, implosions, and other short pulse sources producing background due to hot electrons, hard x-rays, neutrons, and gammas)
Single MCP
Bateman, NIM, 1977

## Slide 2: Beyond Henke: 10x higher PC Q.E. than current ≈ 1%
Existing CsI:
Frumkin, Phys. Rev. A, 1993
Boutbol, JAP, 1999
PC in form of thick MCP
hn
Grid
Future: Thick MCP Photocathode?
Time-discriminating detectors will be needed even at high photon energy when sources to be backlit or other sources have strong self-emission (hohlraums, implosions, and other short pulse sources producing background due to hot electrons, hard x-rays, neutrons, and gammas)
L/D = 10
To Streak Camera, DIXI

## Slide 3: Beyond Henke: 10x higher Q.E. MCPs and photocathodes at 20- 100 keV
Shikhaliev, RSI (1997)
Unity gain photocathode (DC)
Electron multiplier MCP (Gated)
hn
phosphor
Example: Two MCP (Proximity focus coupling)
N. Izumi, 2011
Achievable: ~10% QE @ 100 keV
Increase channel wall thickness

## Slide 4: Flat MCP sensitivity between 10 and 600 keV has been reported previously
1 10 100 1000
From Wiza, NIM, 1979
Photon Energy (keV)

## Slide 5: However, sensitivity is flat because number of primary interactions increases to compensate for Q.E. dropping
For hn between 150 and 500 keV:
Signal ~ Range of electrons/x-ray mfp ~ (hn – I.P. Pb K edge)1.6/(hn)2.0
Range of 100 keV electron = 66 µm in MCP Pb-doped glass
Drop in x-ray interaction probability compensated by increase in primary range and number of secondaries escaping into pores
Leads to predicted almost flat MCP response above 150 keV