## Slide 1
Implementation of a Thomson Parabola on OMEGA for plasma-nuclear and ablator-ion studies
J. Cobble, N. Sinenian and D. Mastrosimone

## Slide 2
Plasma nuclear science - high-resolution ion (spectral) measurements
  TT - a (0- 4.0 MeV)
  T 3He - a (0- 12.1 MeV)
  p 11B - a (0- 8.7 MeV)
Survey of heavy ablator-ions for measurements of total ablator-ion energy loss
  CH, SiO2 and CD-cryo
Other possible applications
  Fast-ignition
  Backlighting in OMEGA target chamber
TPIE complements the existing OMEGA charged-particle diagnostics suite and opens the door to new physics studies

## Slide 3: TPIE has successfully measured heavy-ion spectra on EP, and has more recently been demonstrated on OMEGA
OMEGA-EP (short-pulse)
J. Cobble, et. al., Rev. Sci Instrum. (2011)
B
E
CR-39: variable position
Pinhole assembly

## Slide 4: On OMEGA, the high flux of low-energy ions hinders proper operation; filtering was used to remove this background
Observed background on TPIE was mitigated
(Demonstrated on cryo-ride along PI: Sangster)
1.5 um of Mylar on CR-39
No filtering on CR-39
OMEGA Shot 64680
(First Data Acquired on MIT-NLUF)

## Slide 5: Filtering capability has been added to TPIE for proper operation on OMEGA
0.9-1.5 um Mylar filter is sufficient for most cases; this has little impact on the low-energy cutoff of the instrument
CR-39
Filter pack
assembly
New goalposts
Existing
base

## Slide 6: A new magnet is being implemented to measure lower-energy particles (e.g. TT- a studies)
The (1.65 kG) magnet allows measurements of
protons (or fully ionized 4He) down to ~ 250 keV
Same form-factor as original magnet
1650 G peak field strength
Now have option for 1.65kG, 5.6kG and 8.4kG field strengths
TCC
B

## Slide 7: Summary
TPIE now operational on OMEGA
Filter / magnet selection will be available on SRFs in coming week(s)
Use on tritium shots approved/supported by J. Cobble and G. Pien
  (Image plates must be cleaned prior to removal)