## Slide 1: Hot-Electron Preheat and Energy Deposition in Direct-Drive Implosion Experiments at the National Ignition Facility
A. A. Solodov et al.
University of Rochester
Laboratory for Laser Energetics
48th Anomalous Absorption Conference
Telluride, CO
9–14 June 2019

## Slide 2: Hot-electron preheat and energy deposition in the unablated shell have been measured in polar-direct-drive (PDD) implosions on the NIF
Hot-electron transport in NIF PDD implosions has been studied by comparing hard x-ray (HXR) production in all-plastic implosions with multilayered implosions
The goal is to diagnose the hot-electron deposition profile in the imploding shell
Measurements indicate that 0.280.05% of laser energy is deposited in the unablated shell; 0.10.04% is deposited in the outer 20% portion and 0.180.03% is deposited in the inner 80% of the imploding shell
Hot-electron preheat mitigation using mid-Z layers and laser frequency detuning/bandwidth strategies are being explored.*

## Slide 3
M. J. Rosenberg, A. R. Christopherson, R. Betti, M. Stoeckl, W. Seka, R. Epstein, R. K. Follett,
P. B. Radha, S. P. Regan, D. H. Froula, and V. N. Goncharov
University of Rochester
Laboratory for Laser Energetics
J. F. Myatt
University of Alberta
M. Hohenberger, B. Bachmann, and P. Michel
Lawrence Livermore National Laboratory

## Slide 4: Hot-electron preheat can degrade fuel compression in direct-drive ignition designs
Fuel compression is negatively affected if more than ~0.15% of laser energy is coupled into fuel preheat**
If electron divergence is large, only ~25% of electrons intersect the cold fuel†
Electrons below ~50 keV are stopped in the ablator
there is a limit of ~0.7% laser energy into the hot electrons generated
Motivation

## Slide 5: Hot-electron transport in NIF PDD implosions was studied by comparing HXR between all-plastic and multilayered implosions
Different buried depths and thicknesses of the Ge-doped layer are examined to diagnose the hot-electron deposition profile in the imploding shell.

## Slide 6: The energy deposited into a payload can be inferred by subtracting the all-CH HXR from the HXR of a Ge-doped layered target
Preheat formula:*
is taken from theory; it is proportional to , depends on Thot, and logarithmically on plasma density
and are HXR measurements

## Slide 7: The experiments use thicker shells and higher-adiabat implosions than in the standard PDD design* to reduce possible hydro instabilities
 | NIF ignition scale | These experiments
Ln (μm) | 600 | 400
Te (keV) | 3.5 to 5 | 3.2
IL (W/cm2) | (6 to 8) 1014 | (4 to 8) 1014
 | NIF ignition scale | These experiments
Ln (μm) | 600 | 400
Te (keV) | 3.5 to 5 | 3.2
IL (W/cm2) |  | 
Simulated plasma conditions at nc/4

## Slide 8: Time-resolved scattered-light spectra indicate that LPI is similar between the all-CH and Ge-doped payload implosions
LPI is dominated by SRS at nc/4 and at lower densities
Up to ~25% variation in SRS is observed in some shots, associated with power variation in the nearest beam quads
Similar LPI similar hot-electron source

## Slide 9: The hard x-ray measurement recorded with the FFLEX* diagnostic shows enhanced HXR emission with the Ge dopant
THXR = Thot ≈ 50 keV

## Slide 10: Time-integrated penumbral images* show hard x-ray variation with polar angle

## Slide 11: The energy deposition in different parts of the imploding shell has been found
Total hot-electron coupled energy (kJ) | 10.12 kJ | 9.52 kJ | 10.32 kJ | 10.22 kJ
% of laser energy | 1.40.3% | 1.40.3% | 1.40.3% | 1.40.3%
Energy into Ge-doped layer (kJ) | 2.00.4 kJ | 1.10.3 kJ | 1.00.3 kJ | 1.20.3 kJ
% of laser energy | 0.280.05% | 0.170.03% | 0.140.03% | 0.160.03%
Total hot-electron coupled energy (kJ) |  |  |  | 
% of laser energy |  |  |  | 
Energy into Ge-doped layer (kJ) |  |  |  | 
% of laser energy |  |  |  | 
Targets show consistent total hot-electron production

## Slide 12: The energy deposition profile in the imploding shell has been inferred
About a quarter of total hot-electron energy coupled to the implosion is coupled to the unablated shell, indicating a wide angular divergence of hot electrons

## Slide 13: OMEGA and NIF experiments show roughly similar preheat per mass, even though implosion conditions are different (not hydro-equivalent)
The difference in intensity, and doped/undoped layer thickness ratio complicates a direct comparison; OMEGA experiments hydro-equivalent to the NIF design are proposed for FY20.

## Slide 14: Hot-electron preheat and energy deposition in the unablated shell have been measured in polar direct-drive (PDD) implosions on the NIF
Hot-electron transport in NIF PDD implosions has been studied by comparing hard x-ray (HXR) production in all-plastic implosions with multilayered implosions
The goal is to diagnose the hot-electron deposition profile in the imploding shell
Measurements indicate that 0.280.05% of laser energy is deposited in the unablated shell; 0.10.04% is deposited in the outer 20% portion and 0.180.03% is deposited in the inner 80% of the imploding shell
Hot-electron preheat mitigation using mid-Z layers and laser frequency detuning/bandwidth strategies are being explored.*