## Slide 1: Contamination Control in the Target Fabrication Cleanroom at the National Ignition Facility
T. Braun1, B. Butlin1, E. Piceno1, K. Clark2, E. Giraldez2, S. Baxamusa1, M. Schoff2, A. Nikroo1, M. Stadermann1 1: LLNL, 2: General Atomics
April 26th 2019
23rd Target Fabrication Specialist Meeting
Annapolis, Maryland

## Slide 2: Particles on NIF target capsules can cause instabilities that degrade performance
Images: Steve Haan, LLNL
Video: Louisa Pickworth, LLNL

## Slide 3: NIF Target assembly is performed in a class 100 cleanroom to produce targets for ICF platform
Class 100 cleanroom
It is crucial that cleanliness levels are measured & tracked and sources of contamination (internal or external) are identified and mitigated

## Slide 4: We experienced increased frequency in cleanliness issues which became the primary driver of assembly process issues
Debris exceeded specifications and resulted in lost targets in a few cases and re-work in many cases.
Issues also observed on targets fielded on NIF
We began a systematic effort to identify and mitigate the sources
  Internal sources
  External sources (components)
Tilted Fill tube &
Particles
32 particles located on the capsule
Fill tube
cleanliness
We collect metrics that help us understand issues and help us prioritize our resources
Tally of all issues over 4 months in FY2018
Debris on hohlraum (external source)
C. Walters
Determination of the Location of Particles on Targets Fielded on NIF via Parallax X-ray Imaging
B. Butlin
Overview of Target Production Planning Efforts for the National Ignition Facility (NIF)

## Slide 5: We began systematic data collection and analysis of air borne particles in various parts of assembly floor
A comprehensive particle counting system has been set up that measures airborne particles throughout the clean room and at various work stations.
Live data can be accessed through internal wiki
Class 100/ISO 5
Class 10000/ ISO 7
Hohlraum line
Capsule line
Tent line
Final Ass.

## Slide 6: We are able to correlate particle creation to time of day and personnel
Airborne particle count increases with personnel entering and exiting the clean room
Work hours
Work hours
Work hours
Work hours

## Slide 7: In addition to airborne particle measurement we set up an automated wafer particle analysis
Wafer holder was designed to fit the existing tent metrology system which minimized required modifications to the setup.

## Slide 8: In addition to airborne particle measurement we set up an automated wafer particle analysis
Realtime run of particle analysis on wafer

## Slide 9: Weekly bright light inspection of each station allows tracking cleanliness process over time
Bright light inspections at each station allow us to quickly:
  Track cleanliness progress
  Make corrections as needed by prioritizing resources towards that station.
One calendar week

## Slide 10
A significant external source of particles entering the cleanroom appeared to be on target components
Debris on Hohlraums as received
Debris on Hohlraum packaging
Debris was found on many parts in proximity to the capsule!
LEHs
TMPs
Hohlraums
Diagnostic Bands

## Slide 11
We examined debris observed on as received components to identify the source and a mitigation
Edge of LEH
hohlraum
particles

## Slide 12
Si peak
Analysis of particles and holders indicates that contamination might come from packaging
FTIR analysis of particles and packaging
Hohlraum packaging

## Slide 13: In cooperation with General Atomics, we have designed a cleanable universal packaging container
New universal packaging container is cleanable and can be used for different parts, saving money and effort hours
The design was inspired from the current containers used in the NIF Optics Assembly Building
Container can be used for different parts

## Slide 14: We have extended our cleanliness tracking to work with GA components
    Closely working with General Atomics allow both groups to track and improve cleanliness
    GA is constantly improving their component cleaning process for parts. Overall parts are coming in cleaner.
    LEH parts are now packaged differently, visual results looked excellent!
Chart: LLNL incoming inspection for hohlraums – particle count

## Slide 15: Prioritizing our resources towards cleanliness has led to a significant decrease in cleanliness issues
Chart: 
| FY18Q3 | FY18Q4 | FY19Q1 | FY19Q2
 | 47 | 18 | 9 | 5
Tally of all cleanliness issues over the last four quarters in FY2018 / FY2019

## Slide 16: We have implemented a number of changes and best practices to track and avoid drift in the cleanliness process both at LLNL and GA
Identified external and internal issues
  Packaging and PetG containers are being optimized
  Shipping
  Component inspection
  Gowning
  Air Outlets
Facility testing
  We are continuously monitoring cleanliness
  We are now able to monitor each workstation separately
We have many things that are done correctly
  Cleanliness issues are decreasing
  Personnel comes forward if they see something

## Slide 18: Comparisons of Classifications
Target Fabrication R1600 Cleanroom